## Slide 1
YOLO Ensemble for UAV-based Multispectral Defect Detection in Wind Turbine Components
Serhii Svystun¹, Pavlo Radiuk¹, Oleksandr Melnychenko¹, Oleg Savenko¹, Anatoliy Sachenko²
¹ Khmelnytskyi National University, Ukraine, ² West Ukrainian National University, Ukraine
INTRODUCTION
Wind power plants critical in renewable energy transition
Efficiency depends on timely maintenance and defect prevention
Minor defects can pose substantial economic and safety risks
UAVs with sensors efficiently collect visual information
MAJOR CONTRIBUTIONS
Multispectral image fusion (RGB + thermal IR)
Novel ensemble learning approach with bounding box fusion
Comprehensive evaluation showing superior performance
METHODS
Our approach integrates high-resolution visible (RGB) and thermal (IR) data channels through:
Data acquisition
Multispectral image fusion
Parallel model training
Ensemble fusion
RESULTS
Training dataset: Blade30 dataset (1,102 images) + 670 overheating images
ENSEMBLE FUSION ALGORITHM
Intelligent combination of predictions using bounding box fusion:
Merges overlapping detections of the same class
Preserves unique findings from each model
Uses weighted averages and Non-Maximum Suppression
CONCLUSIONS
Our ensemble approach achieves superior performance in detecting wind turbine defects compared to single-model approaches
Integration of thermal data is particularly impactful for identifying overheating and subsurface defects
Future research will focus on optimizing the ensemble for real-time edge deployment and incorporating advanced data fusion techniques
svystuns@khmnu.edu.ua, radiukp@khmnu.edu.ua, melnychenko@khmnu.edu.ua, savenko_oleg_st@ukr.net, as@wunu.edu.ua
Model | mAP@.5 | mAP@.5:.95 | F1-Score
YOLOv8 (Single) | 0.91 | 0.76 | 0.88
Faster R-CNN | 0.89 | 0.74 | -
Cascade R-CNN | 0.90 | 0.75 | -
Our Ensemble | 0.93 | 0.79 | 0.90
Key improvements:
• Mean mAP@.5: 0.91 → 0.93 (2.2% improvement)
• F1-score for "Cracks": 0.90 → 0.92
• F1-score for "Overheating": 0.86 → 0.89
Data Collection and Model Training:
RGB Channel: High-resolution optical images (4K/6K)
IR Channel: Thermal images for temperature anomalies
Three defect classes: Cracks (C¹), Corrosion (C²), Overheating (C³)